125KHz RFID Fixed Reader RDM6520

Photos:

Main Applications:

- Access Control

- Time Attendance

- Building Management

- Automatic identification

- Product anti forgery

- Guest Registration System

- People Tracking

- Asset Tracking

- Manufacturing

- Returnable Transit Items

Key Features:

- Available in 125KHz Radio Frequency

- RS232,RS485, Wiegand26,34 interface

- EM4100, EM4200 & TK4100 compliant

Easy to Use and Deploy

Specification:

The 125KHz RFID Fixed reader RDM6520 is a Low Frequency (L F) Proximity reader, which is available to EM4100, EM4200, TK4100 and compatible cards, With RRS232,RS485, Wiegand26,34 interface optional, RDM6520 is easy to use and deploy, fast and convenient to connect with other controlling devices

Until now, RDM6520 Reader has been widely used in applications such as access control system, time attendance, guest registration system and identification authentication field etc.

Communication description:

| WEIGANG26 : | RS232/RS485 : |
| --- | --- |
| RED: | DC9~12V | RED: | +9V~12VDC |
| BLACK: | GND | BLACK: | GND |
| GREEN: | DATA0 | GREEN: | TX(RS232)/R+(RS485) |
| WHITE: | DATA1 | WHITE: | RX(RS232)/R-(RS485) |
| BROWN: | HOLD | BROWN: | HOLD |
| BLUE: | LED(Touch Down) | BLUE: | LED(Touch Down) |
| GREY: | BUZ(Touch Down) | GREY: | BUZ(Touch Down) |
| YELLOW: | NC | YELLOW: | NC |

Technical Specification:

| Frequency | 125KHz |
| --- | --- |
| Baud Rate | I9600/19200(RS232/RS485) |
| Interface | RS232/RS485/Wiegand26/Wiegand34 |
| Support card | EM4100, EM4200, TK4100 etc. |
| Power Supply | DC 9V ～ 12V(±5%) |
| Current | < 60mA |
| Maximum Read Distance | 8 cm(Tag dependent) |
| Audio/Visual Indication | Internal LED and buzzer |
| Housing Material | ABS Housing |
| Operating Temperature | -10℃ to +70℃ |
| Storage Temperature | -20℃ to +80℃ |
| Humidity | 0～95% |
| Dimension | 80mm*43mm*13mm |
| Weight | 30g |

Ordering information:

To order, please use exact Model Number

| Model Number | Interface | Descriptions |
| --- | --- | --- |
| RDM6520-W | Wiegand26 | Serial No.Read-Only |
| RDM6520-G | Wiegand34 | Serial No.Read-Only |
| RDM6520-S | RS232 | Serial No.Read-Only |
| RDM6520-R | RS485 | Serial No.Read-Only |

Note: Other housings attached are optional , if any other product requirement, please contact us @ sales@datarfid.com directly.

# Text boxes

RDM6580

RDM6540

RDM6510

RDM6560