13.56MHz RFID Reader Writer Module RDM880

Photos:

Main Applications:                        Pin Definition:

| J1-PIN1 | Obligate(RFU) |
| --- | --- |
| PIN2 | Obligate(RFU) |
| PIN3 | LEDG |
| PIN4 | LEDR |
| PIN5 | BUZ |
| J2- PIN1 | RESET |
| PIN2 | RXD/DATA1 |
| PIN3 | TXD/DATA0 |
| PIN4 | GND |
| PIN5 | +5V(DC) |
| J3-PIN1 | ANTENNA- |
| PIN2 | ANTENNA+ |

- Access Control/Time Attendance

- Handy Terminal

- Automatic Identification

- Product Anti Forgery

- Guest Registration System

- People & Asset Tracking

- Returnable Transit Items

- Custom-Built For System Integrators

Key Features:

- Available in 13.56MHz Radio Frequency

- ISO14443A, B, ISO15693 compliant

- RS232, RS485, TTL interface

- Easy to Integrate, Compact Size

- High Performance, Low Cost

- RoHS, CE, FCC Compliant

Specification:

Designed for the applications of 13.56 MHz technology for handy terminal or custom-built for system integrators, RDM880 is a high frequency (HF) 13.56 MHz RFID reader writer module, which is applicable to ISO14443A, ISO14443B and ISO15693 standards.

Configured with RS232, RS485, TTL interface for option, it is easy and convenient to connect the module to an controlling device. With RoHS, CE, FCC certificates, this module has been widely sold all over the world.

With our free Software Development Kit (SDK )including User Manual, API, Demo Code etc, you can make a fast development and integration for the device. The DLL is available to Windows98, Windows 2000,Windows XP, Vista, Windows NT and Linux and the sample code can be programmed by VC++,Delphi or VB.

Technical Specification:

| Frequency | 13.56MHz |
| --- | --- |
| Chips | MFRC500, MFRC400, MFRC531, MFRC632 |
| Standard | ISO/IEC14443A/B, ISO15693, ISO18092 |
| Interface | RS232/RS485/TTL/ABA |
| Support card | Mifare 1K, Mifare 4K, Mifare Ultralight, Mifare Pro, NFC, AT88RF020, 66CL160S, SR176, SRIX4K(Type-B), I-Code2, TI RFID Tag-it HF-I, EM4135, EM4034 etc. |
| Baud Rate | 9600/115200 bps（configurable default 9600bps) |
| Power Supply | DC 5V(±5%) |
| Current | <70mA |
| Maximum Read Distance | Mifare: 8 cm（Tag dependent） I-Code2: 8 cm |
| Audio/Visual Indication | No |
| Antenna | External ( see HF antenna optional for RF module) |
| Operating Temperature | -10℃ to +70℃ |
| Storage Temperature | -20℃ to +80℃ |
| Humidity | 0～95% |
| Dimension | 39mm*19mm*9mm |

Ordering information:

To order, please use exact Model Number

| Model Number | Interface | Descriptions |
| --- | --- | --- |
| RDM880-S-A | RS232 | ISO14443A Read & Write |
| RDM880-S-C | RS232 | ISO15693 Read & Write |
| RDM880-S-E | RS232 | ISO14443A+B+15693 Read & Write |
| RDM880-R-A | RS485 | ISO14443A Read & Write |
| RDM880-R-C | RS485 | ISO15693 Read & Write |
| RDM880-R-E | RS485 | ISO14443A+B+15693 Read & Write |
| RDM880-T-A | TTL | ISO14443A Read & Write |
| RDM880-T--C | TTL | ISO15693 Read & Write |
| RDM880-T--E | TTL | ISO14443A+B+15693 Read & Write |
| RDM880-U-A | USB | ISO14443A Read & Write |
| RDM880-U-E | USB | ISO14443A+B+15693 Read & Write |
| RDM880-NFC | Serial port | ISO14443A+ ISO18092 Read & Write |

Optional size of Configurable antennas

| Model | B01 | B02 | B03 | B04 | B05 | B06 |
| --- | --- | --- | --- | --- | --- | --- |
| Size(mm) | 20*30 | 20*40 | 34*34 | 49*55 | 65*90 | 54*73-2.0 |

Connecting the RDM880 Module

- Power Supply Options

RDM880 powered at J2-5 = DC5V(5%)

DC5V

GND

Note: In the configuration shown above, The Module requires a regulated input voltage in DC5V input to J2-5(an input in this configuration).

- Connect ion Of RDM880 To PC

connection: RDM880 TO PC

GND

RDM880 Module     RXD

TXD

Note: In addition to the signals connections, the host must supply input voltage. See Figure 8. If the module’s interface is RS232, it’s output format needs to be converted by a chip when the module is connected to pc.

- Antenna Connections

All Models of the RDM880 have two internal antennas that can be enabled by connecting J3-1 and J3-2 .

Connecting the Antenna

J3-1  J3-2

- LED and Buzzer Connections

LED and Buzzer Connections

Note: For any interface of RDM880 modules, the LEDR pin is connected to the red LED, and the LEDG pin is connected to a green LED, the BUZ pin is connected to the buzzer.

PIN CONNECTION Instruction

RS232/TTL interface instruction

ANTENNA +

ANTENNA -

BUZ                                           +5V(DC)

LEDR                                          GND

LEDG                                          TXD（R+）

NC                                             RXD（R-）

NC                                             RESET

Pin Descriptions (Read & Write)

| Pin | Name | Description |
| --- | --- | --- |
| J1-1 | NC | Obligate |
| J1-2 | NC | Obligate |
| J1-3 | LEDG | It is usually low level, this pin can control the LED when the low level is connected to GND. |
| J1-4 | LEDR | It is usually high level which can control the LED when the low level is connected to GND. |
| J1-5 | BUZ | It is usually low level, this pin can control the buzzer when the high level is connected to GND. |
| J2-1 | RESET | Reset |
| J2-2 | RXD | Connects with R1OUT(a 232PWL drive chip) |
| J2-3 | TXD | Connects with T1IN a 232PWL drive chip) |
| J2-4 | GND | Connects with the cathode of the power supply |
| J2-5 | +5V(DC) | Connects with the anode of the power supply |
| J3-1 | ANTENNA - | Connects with the antenna |
| J3-2 | ANTENNA + | Connects with the antenna |

Pin Descriptions(Read Only)

| Pin | Name | Description |
| --- | --- | --- |
| J1-1 | NC | Obligate |
| J1-2 | NC | Obligate |
| J1-3 | LEDG | It is usually low level, punching a card will discontinue the high level signal. |
| J1-4 | LEDR | It is usually high level, punching a card will discontinue the low level signal. |
| J1-5 | BUZ | It is usually low level, punching a card will expand the time of the 88US high level signal. |
| J2-1 | RESET | Reset |
| J2-2 | NC | Obligate |
| J2-3 | TXD | Connects with T1IN a 232PWL drive chip) |
| J2-4 | GND | Connects with the cathode of the power supply |
| J2-5 | +5V(DC) | Connects with the anode of the power supply |
| J3-1 | ANTENNA - | Connects with the antenna |
| J3-2 | ANTENNA + | Connects with the antenna |

RS232/RS485 Interface Instruction

RS232/RS485 interface instruction

ANTENNA +

ANTENNA -

BUZ                                           +5V(DC)

LEDR                                          GND

LEDG                                          TXD（R+）

NC                                             RXD（R-）

NC                                             RESET

Pin Descriptions (Read & Write)

| Pin | Name | Description |
| --- | --- | --- |
| J1-1 | NC | Obligate |
| J1-2 | NC | Obligate |
| J1-3 | LEDG | It is usually low level, this pin can control the LED when the low level is connected to GND. |
| J1-4 | LEDR | It is usually high level which can control the LED when the low level is connected to GND. |
| J1-5 | BUZ | It is usually low level, this pin can control the buzzer when the high level is connected to GND |
| J2-1 | RESET | Reset |
| J2-2 | RXD | Receive Data（R+） |
| J2-3 | TXD | Transmit Data（R-） |
| J2-4 | GND | Connects with the cathode of the power supply |
| J2-5 | +5V(DC) | Connects with the anode of the power supply |
| J3-1 | ANTENNA - | Connects with the antenna |
| J3-2 | ANTENNA + | Connects with the antenna |

Pin Descriptions (Read Only)

| Pin | Name | Description |
| --- | --- | --- |
| J1-1 | NC | Obligate |
| J1-2 | NC | Obligate |
| J1-3 | LEDG | It is usually low level, punching a card will expand the time of the 88US high level signal. |
| J1-4 | LEDR | It is usually high level, punching a card will expand the time of the 88US low level signal. |
| J1-5 | BUZ | It is usually low level, punching a card will expand the time of the 88US high level signal. |
| J2-1 | RESET | Reset |
| J2-2 | RXD | Receive Data（R+） |
| J2-3 | TXD | Transmit Data（R-） |
| J2-4 | GND | Connects with the cathode of the power supply |
| J2-5 | +5V(DC) | Connects with the anode of the power supply |
| J3-1 | ANTENNA - | Connects with the antenna |
| J3-2 | ANTENNA + | Connects with the antenna |

3.2.1 RS232 Format Interface

RS232 Format Interface

| 02 | 10 ASCII Data Characters | Checksum | 03 |
| --- | --- | --- | --- |

a. 9600bps, N,8,1.

b. Checksum: The byte marked with Checksum go for XOR Parity check of the Card Number. Checksum = CR + LF.

EXAMPLE:

Card Number: 62 E3 08 6C ED (High bit ---- Low bit)

Output ASCII Code: 02H 36H 32H 45H 33H 30H 38 H 36H 43H 45H 44H 30H 28H 03H

Checksum: 62H xor E3H xor 08H xor 6CH xor EDH = 08H

SO: CR = 30h LF = 38H

3.2.2 RS232 Format Timing

Figure 7 RS232 format timing